## Slide 1
Linux
Miscellaneous
lsblk · df · du · dmidecode · uname · free · ps · top · ip · ss · find · watch · grep
Linux Tizim Boshqaruvi — Amaliy Dars

## Slide 2
Mavzular Ro'yxati
① Disk & Saqlash lsblk, df, du
② Hardware dmidecode
③ Tizim Ma'lumotlari uname, uptime, free
④ Jarayonlar ps, top
⑤ Tarmoq ip, ss
⑥ Fayl Qidiruv find
⑦ Qo'shimcha Asboblar watch, tee, xargs, grep

## Slide 3
Disk va Saqlash
lsblk · df · du

## Slide 4
lsblk — Block Qurilmalar Ro'yxati
lsblk (list block devices) buyrug'i tizimga ulangan barcha disk, partition, USB va virtual
saqlash qurilmalarini daraxt ko'rinishida ko'rsatadi. mount qilish shart emas.
Asosiy foydalanish:
$ lsblk
NAME MAJ:MIN RM SIZE RO TYPE MOUNTPOINT
sda 8:0 0 50G 0 disk
├─sda1 8:1 0 49G 0 part /
└─sda2 8:2 0 1G 0 part [SWAP]
sdb 8:16 1 16G 0 disk
└─sdb1 8:17 1 16G 0 part /media/usb
sr0 11:0 1 1024M 0 rom
Ustunlar: NAME=qurilma nomi RM=removable RO=read-only TYPE=disk|part|rom

## Slide 5
lsblk — Foydali Opsiyalar
-f : fayl tizimi turi va UUID ko'rsatish
$ lsblk -f
NAME FSTYPE LABEL UUID MOUNTPOINT
sda
├─sda1 ext4 a1b2c3d4-e5f6-7890-abcd-ef1234567890 /
└─sda2 swap f6e5d4c3-b2a1-... [SWAP]
Faqat kerakli ustunlarni tanlash (-o):
$ lsblk -o NAME,SIZE,TYPE,FSTYPE,MOUNTPOINT,LABEL
NAME SIZE TYPE FSTYPE MOUNTPOINT LABEL
sda 50G disk
├─sda1 49G part ext4 /
└─sda2 1G part swap [SWAP]
-J JSON formatida chiqarish (skriptlar uchun)
-m ruxsatlar va egalik ma'lumotlari
-p to'liq yo'l ko'rsatish (/dev/sda1 emas — /dev/sda1)
-t topology: daraxt munosabatlarini aniqroq ko'rsatish
-l daraxt emas, oddiy ro'yxat (list) ko'rinishida

## Slide 6
df — Disk Bo'sh Joyini Ko'rish
df (disk free) har bir o'rnatilgan fayl tizimida qancha joy bor va qanchasi ishlatilganini ko'rsatadi.
df -h (human-readable: K/M/G/T formatida):
$ df -h
Filesystem Size Used Avail Use% Mounted on
/dev/sda1 49G 12G 35G 26% /
tmpfs 1.9G 0 1.9G 0% /dev/shm
/dev/sda1 100M 31M 70M 31% /boot
tmpfs 390M 1.2M 388M 1% /run
Foydali variantlar:
$ df -hT # fayl tizimi turi ham (ext4, tmpfs, xfs...)
$ df -i # inode ishlatilishi (fayllar soni limiti)
$ df -h /home # faqat bitta mount point
$ df -h --total # oxirida umumiy jami
Eslatma: df saqlash qurilmasining umumiy holini ko'rsatadi. Aniq katalog hajmi uchun — du.

## Slide 7
du — Katalog va Fayl Hajmini Hisoblash
du (disk usage) katalog ichidagi barcha fayllarni rekursiv o'qib, haqiqiy disk sarfini hisoblaydi.
Asosiy misol — katalog jami hajmi:
$ du -sh /var/log
156M /var/log
$ du -sh /var/*
2.3G /var/cache
156M /var/log
48M /var/lib
Eng katta kataloglar — top 10:
$ du -sh /* 2>/dev/null \
| sort -rh \
| head -10
8.4G /usr
3.1G /var
1.2G /home
512M /lib
Chuqurlik chegaralash (--max-depth):
$ du -h --max-depth=2 /var # 2 darajagacha
$ du -ah /home/user # barcha fayllar alohida-alohida
$ du -ch /var/log/*.log # faqat .log fayllar + jami
du vs df: df = fayl tizimining umumiy sarfi | du = konkret katalog ichidagi haqiqiy sarfi

## Slide 8
Hardware Ma'lumotlari
dmidecode

## Slide 9
dmidecode — BIOS / SMBIOS Ma'lumotlari
dmidecode DMI (Desktop Management Interface) ma'lumotlar bazasini o'qib, apparat haqida to'liq
ma'lumot beradi. Root huquqi kerak. Haqiqiy apparat o'qiladi — lshw/lscpu dan farqli o'laroq.
Eng ko'p ishlatiladigan turlar (-t type):
Type | Ma'lumot | Buyruq
0 | BIOS versiyasi va sanasi | sudo dmidecode -t 0
1 | Tizim — ishlab chiqaruvchi, model, serial | sudo dmidecode -t 1
4 | Processor (CPU modeli, yadro soni, tezligi) | sudo dmidecode -t 4
16 | Jismoniy xotira qurilmasi (RAM slots) | sudo dmidecode -t 16
17 | Har bir RAM modul — hajm, tezlik, tur | sudo dmidecode -t 17

## Slide 10
dmidecode — Amaliy Misollar
RAM ma'lumotlari (har bir modul):
$ sudo dmidecode -t 17 | grep -E 'Size|Speed|Type:|Manufacturer'
Size: 8192 MB
Type: DDR4
Speed: 2400 MT/s
Manufacturer: Samsung
CPU ma'lumotlari:
$ sudo dmidecode -t 4 | grep -E 'Version|Core Count|Current Speed'
Version: Intel(R) Core(TM) i7-8750H CPU @ 2.20GHz
Core Count: 6
Current Speed: 2200 MHz
BIOS versiyasi va sanasi:
$ sudo dmidecode -t 0 | grep -E 'Version|Release Date'
Version: F.75
Release Date: 11/02/2022

## Slide 11
Tizim Ma'lumotlari
uname · uptime · free

## Slide 12
uname — Kernel va Arxitektura
uname -a (barcha ma'lumotlar bir satrda):
$ uname -a
Linux server01 5.15.0-76-generic #83-Ubuntu SMP Fri Jun 23 x86_64 GNU/Linux
# |
# └── build raqami
Alohida flaglar:
$ uname -r # kernel versiyasi: 5.15.0-76-generic
$ uname -m # arxitektura: x86_64 (yoki aarch64, armv7l)
$ uname -s # OS nomi: Linux
$ uname -n # hostname
OS versiyasi — /etc/os-release va hostnamectl:
$ cat /etc/os-release | grep -E '^(NAME|VERSION)='
NAME="Ubuntu"
VERSION="22.04.3 LTS (Jammy Jellyfish)"
$ hostnamectl
Static hostname: server01
Icon name: computer-server
Operating System: Ubuntu 22.04.3 LTS
Kernel: Linux 5.15.0-76-generic

## Slide 13
uptime · w · who — Tizim va Sessiya Holati
uptime — tizim qancha vaqt ishladi, load average:
$ uptime
14:32:11 up 12 days, 3:21, 2 users, load average: 0.42, 0.38, 0.35
# 1min 5min 15min
w — kim ulangan va nima qilayapti:
$ w
14:32:11 up 12 days, 2 users, load average: 0.42
USER TTY FROM LOGIN@ IDLE JCPU PCPU WHAT
root pts/0 192.168.1.5 14:20 0.00s 0.12s 0.01s bash
deploy pts/1 192.168.1.8 09:11 1:23m 0.04s 0.04s tail -f app.log
who va last — login tarixi:
$ who # hozir ulangan foydalanuvchilar
$ last | head -10 # oxirgi loginlar va logout vaqtlari
$ last reboot | head -5 # tizim qayta ishga tushirilgan vaqtlar
load average: 1 daqiqalik / 5 daqiqalik / 15 daqiqalik o'rtacha jarayon navbati. CPU yadro sonidan oshsa — tiqilinch.

## Slide 14
free — RAM va Swap Xotira Holati
free joriy xotira holatini ko'rsatadi.
free -h (human-readable):
$ free -h
total used free shared buff/cache available
Mem: 7.7Gi 2.1Gi 3.4Gi 127Mi 2.1Gi 5.2Gi
Swap: 2.0Gi 0B 2.0Gi
total — jismoniy RAM umumiy hajmi
used — hozir ishlatilayotgan xotira
free — hech narsa tegmagan sof bo'sh xotira
buff/cache — kernel tomonidan keshga olingan (bo'shatilishi mumkin)
available — yangi dasturlar uchun HAQIQIY bo'sh joy (free + cache)
Real-vaqt kuzatish va skript uchun:
$ free -h -s 2 # har 2 sekundda yangilash (Ctrl+C bilan to'xtatish)
$ free -m # megabaytda
$ free -b | awk 'NR==2{printf "Used: %.1f%%\n", $3/$2*100}' # foiz

## Slide 15
Jarayonlar va CPU
ps · top

## Slide 16
ps — Jarayonlar Ro'yxati
ps (process status) tizimda ishlaydigan jarayonlar haqida ma'lumot beradi.
ps aux — barcha foydalanuvchilarning barcha jarayonlari:
$ ps aux
USER PID %CPU %MEM VSZ RSS TTY STAT START TIME COMMAND
root 1 0.0 0.1 168932 11288 ? Ss 09:11 0:03 /sbin/init
root 854 0.0 0.2 281104 18492 ? Ss 09:11 0:00 /usr/sbin/sshd
www-data 1234 0.1 0.5 312456 44012 ? S 09:15 0:12 apache2
Foydali kombinatsiyalar:
$ ps aux | grep nginx # nginx jarayonlarini qidirish
$ ps -ef --forest # ota-bola (parent-child) ierarxiyasi
$ ps -p 1234 -o pid,ppid,cmd,%cpu,%mem # bitta PID uchun batafsil
$ ps aux --sort=-%cpu | head -10 # CPU ko'p sarflayotgan top-10
STAT ustuni: S=uxlaydi R=ishlaydi Z=zombie T=to'xtatilgan s=session leader
VSZ = virtual xotira | RSS = haqiqiy RAM sarfi

## Slide 17
top — Real-vaqt Jarayon Monitoru
top — tizim resurslarini real vaqtda ko'rsatadigan interaktiv vosita. Har 3 sekundda yangilanadi.
top ichida klaviatura tugmalari:
Tugma | Vazifasi
P | CPU sarfi bo'yicha tartiblash (standart)
M | RAM sarfi bo'yicha tartiblash
k | Jarayonni o'ldirish (PID so'raydi)
r | Jarayon ustunligini o'zgartirish (renice)
1 | Har bir CPU yadrosini alohida ko'rsatish
q | Chiqish
Skript ichida bir marta o'qish (interaktiv emas):
$ top -bn1 | head -20 # bir iteratsiya, stdout
$ top -bn1 | grep 'Cpu\|Mem' # faqat CPU va RAM satrlari
# htop — top'ning qulay alternativi (sudo apt install htop)
$ htop

## Slide 18
Tarmoq
ip · ss

## Slide 19
ip va ss — Tarmoq Interfeyslari va Portlar
ip addr show — IP manzillar:
$ ip addr show
2: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500
link/ether 00:11:22:33:44:55 brd ff:ff:ff:ff:ff:ff
inet 192.168.1.10/24 brd 192.168.1.255 scope global eth0
ip route show — marshrutlash jadvali:
$ ip route show
default via 192.168.1.1 dev eth0
192.168.1.0/24 dev eth0 proto kernel scope link src 192.168.1.10
ss -tulpn — tinglayotgan portlar (netstat o'rniga):
$ ss -tulpn
Netid State Recv-Q Send-Q Local Address:Port Process
tcp LISTEN 0 128 0.0.0.0:22 users:(("sshd",pid=854))
tcp LISTEN 0 511 0.0.0.0:80 users:(("apache2",pid=1234))
tcp LISTEN 0 70 127.0.0.1:3306 users:(("mysqld",pid=2001))
ss -s qisqacha statistika | ss -tn TCP ulanishlar holati

## Slide 20
Fayl Qidiruv
find

## Slide 21
find — Fayllarni Qidirish
find rekursiv ravishda fayl tizimida qidiradi. Shart (-name, -type, -size, -mtime...) bo'yicha filtrlaydi.
Nom va kengaytma bo'yicha:
$ find /var/log -name "*.log" # barcha .log fayllar
$ find /etc -name "*.conf" -type f # faqat fayllar (papka emas)
$ find /home -iname "readme*" # katta-kichik harf farqsiz
Hajm va vaqt bo'yicha:
$ find /var -size +50M # 50 MB dan katta
$ find / -size +100M -size -1G # 100MB-1GB oralig'i
$ find /home -mtime -7 # oxirgi 7 kun ichida o'zgargan
$ find /tmp -atime +30 # 30 kundan beri ochilmagan
find + exec — topilgan fayllarda buyruq bajarish:
$ find /tmp -type f -name "*.tmp" -exec rm {} \;
$ find /var/log -name "*.log" -size +100M -exec gzip {} \;

## Slide 22
find — Kuchli Kombinatsiyalar
SUID/SGID fayllar — xavfsizlik tekshiruvi:
$ find / -perm -u=s -type f 2>/dev/null # SUID biti o'rnatilgan fayllar
$ find / -perm -g=s -type f 2>/dev/null # SGID biti
Chuqurlik chegaralash:
$ find /etc -maxdepth 1 -type f # faqat to'g'ridan to'g'ri fayllar
$ find / -mindepth 3 -maxdepth 5 -name "*.key"
OR / NOT mantiqiy operatorlar:
$ find /var -name "*.log" -o -name "*.txt" # .log YOKI .txt
$ find /etc ! -name "*.conf" # .conf bo'lmaganlar
$ find . -type f \( -name "*.sh" -o -name "*.py" \) -executable
Topilgan fayllarni boshqa buyruqqa uzatish (xargs bilan):
$ find /var/log -name "*.log" -print0 | xargs -0 grep -l "ERROR"
$ find . -name "*.py" | xargs wc -l | sort -rn | head -10

## Slide 23
Qo'shimcha Foydali Buyruqlar
watch · tee · xargs · grep

## Slide 24
watch · tee · xargs
watch — buyruqni takror-takror bajarish (real-vaqt kuzatish):
$ watch -n 2 'df -h' # har 2 sekundda df -h
$ watch -n 1 'ps aux | grep nginx'
$ watch -d -n 3 'free -h' # -d o'zgargan qatorlarni ajratib ko'rsatadi
tee — stdout ni ham ekranga, ham faylga bir vaqtda yozish:
$ df -h | tee disk_report.txt # ko'rsatadi + saqlaydi
$ df -h | tee -a disk_report.txt # -a : faylga qo'shib yozadi
$ sudo apt upgrade 2>&1 | tee upgrade.log # stderr ham qo'shib
xargs — stdin dan argument yaratib buyruqqa uzatish:
$ echo 'sda sdb sdc' | xargs -n1 lsblk # har bir argument alohida
$ cat pids.txt | xargs kill -9 # fayl ichidagi PID larni o'ldirish
$ ls *.log | xargs -P4 gzip # 4 parallel jarayonda siqish
$ find . -name '*.bak' | xargs rm -v # find natijasini rm ga uzatish
xargs -0 va find -print0 birgalikda ishlatiladi — fayl nomlarida bo'shliq bo'lsa ham xavfsiz.

## Slide 25
grep va Pipe — Kuchli Kombinatsiyalar
grep — satrlarni filtrlash:
$ grep -r "error" /var/log/ # rekursiv qidirish
$ grep -i "failed" /var/log/auth.log # -i: katta-kichik farqsiz
$ grep -v "^#" /etc/ssh/sshd_config # -v: mos kelmaydiganlar
$ grep -n "PermitRoot" /etc/sshd_config # -n: qator raqami bilan
Amaliy pipe kombinatsiyalari:
# Eng ko'p xato qaydlarini topish
$ grep -i 'error\|fail' /var/log/syslog | tail -20
# Biror portga ulanishlar soni
$ ss -tn | grep ':80' | awk '{print $5}' | cut -d: -f1 \
| sort | uniq -c | sort -rn | head -10
# Tizimda kim root bilan kirishga uringan
$ grep 'Failed password for root' /var/log/auth.log \
| awk '{print $11}' | sort | uniq -c | sort -rn
awk '{print $N}' N-ustunni oladi | cut -d: -f1 ikki nuqta ajratuvchi, 1-maydon | uniq -c takrorlanish soni

## Slide 26
Xulosa — Buyruqlar Tezkor Ma'lumotnomasi
Buyruq | Asosiy vazifasi | Eng foydali flag
lsblk | Block qurilmalar ro'yxati | -f -o -J
df | Disk bo'sh joyi (mount pointlar) | -h -hT -i
du | Katalog hajmi | -sh --max-depth -ah
dmidecode | BIOS/RAM/CPU apparat ma'lumoti | -t 4/17/0
uname | Kernel versiyasi va arxitektura | -r -m -a
uptime/w | Tizim ish vaqti, ulanishlar | -p
free | RAM va Swap holati | -h -s N
ps | Jarayonlar ro'yxati | aux --forest
top | Real-vaqt jarayon monitoru | -bn1
ip | Tarmoq interfeyslari va marshrutlash | addr route link
ss | Portlar va socketlar | -tulpn -s
find | Rekursiv fayl qidirish | -name -size -mtime -exec
watch | Buyruqni takrorli bajarish | -n N -d
tee | stdout → ekran + fayl | -a
xargs | stdin dan argument yasash | -n -P -0